## Slide 1: Lecture 5
Number System

## Slide 2: Number Systems
Decimal
Binary
Octal
Hexadecimal

## Slide 3: Why do we need various number base conversions
for digital hardware, the natural numbering system is binary (base 2).
but expressing anything in binary causes way too many bits to be used, so , it's not practical.
hexadecimal allows us to use 4x fewer bits, so, it is very useful.
besides no processor uses anything less than 4bits, so, hexadecimal is the most common when expressing numbers in a way that is most suitable for digital hardware.

## Slide 4: Quantities/Counting (1 of 3)
Decimal | Binary | Octal | Hexa- decimal
0 | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 10 | 2 | 2
3 | 11 | 3 | 3
4 | 100 | 4 | 4
5 | 101 | 5 | 5
6 | 110 | 6 | 6
7 | 111 | 7 | 7
p. 33

## Slide 5: Quantities/Counting (2 of 3)
Decimal | Binary | Octal | Hexa- decimal
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F

## Slide 6: Quantities/Counting (3 of 3)
Decimal | Binary | Octal | Hexa- decimal
16 | 10000 | 20 | 10
17 | 10001 | 21 | 11
18 | 10010 | 22 | 12
19 | 10011 | 23 | 13
20 | 10100 | 24 | 14
21 | 10101 | 25 | 15
22 | 10110 | 26 | 16
23 | 10111 | 27 | 17
Etc.

## Slide 7: Conversion Among Bases
The possibilities:
Hexadecimal
Decimal
Octal
Binary

## Slide 8: Quick Example
2510 = 110012 = 318 = 1916
Base

## Slide 9
12510 => 5 x 100 = 5 2 x 101 = 20 1 x 102 = 100 125
Base
Weight

## Slide 10: Binary to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 11: Binary to Decimal
Technique
  Multiply each bit by 2n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 12: Example
1010112 => 1 x 20 = 1 1 x 21 = 2 0 x 22 = 0 1 x 23 = 8 0 x 24 = 0 1 x 25 = 32
4310
Bit “0”

## Slide 13: Octal to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 14: Octal to Decimal
Technique
  Multiply each bit by 8n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 15: Example
7248 => 4 x 80 = 4 2 x 81 = 16 7 x 82 = 448 46810

## Slide 16: Hexadecimal to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 17: Hexadecimal to Decimal
Technique
  Multiply each bit by 16n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 18: Example
ABC16 => C x 160 = 12 x 1 = 12 B x 161 = 11 x 16 = 176 A x 162 = 10 x 256 = 2560
274810

## Slide 19: Decimal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 20: Decimal to Binary
Technique
  Divide by two, keep track of the remainder
  First remainder is bit 0 (LSB, least-significant bit)
  Second remainder is bit 1
  Etc.

## Slide 21: Example
12510 = ?2
2 125 62 1
2 31 0
2 15 1
2 7 1
2 3 1
2 1 1
2 0 1
12510 = 11111012

## Slide 22: Octal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 23: Octal to Binary
Technique
  Convert each octal digit to a 3-bit equivalent binary representation

## Slide 24: Example
7058 = ?2
7 0 5
111 000 101
7058 = 1110001012

## Slide 25: Hexadecimal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 26: Hexadecimal to Binary
Technique
  Convert each hexadecimal digit to a 4-bit equivalent binary representation

## Slide 27: Example
10AF16 = ?2
1 0 A F
0001 0000 1010 1111
10AF16 = 00010000101011112

## Slide 28: Decimal to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 29: Decimal to Octal
Technique
  Divide by 8
  Keep track of the remainder

## Slide 30: Example
123410 = ?8
8 1234
154 2
8
19 2
8
2 3
8
0 2
123410 = 23228

## Slide 31: Decimal to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 32: Decimal to Hexadecimal
Technique
  Divide by 16
  Keep track of the remainder

## Slide 33: Example
123410 = ?16
123410 = 4D216
16 1234
77 2
16
4 13 = D
16
0 4

## Slide 34: Binary to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 35: Binary to Octal
Technique
  Group bits in threes, starting on right
  Convert to octal digits

## Slide 36: Example
10110101112 = ?8
1 011 010 111
1 3 2 7
10110101112 = 13278

## Slide 37: Binary to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 38: Binary to Hexadecimal
Technique
  Group bits in fours, starting on right
  Convert to hexadecimal digits

## Slide 39: Example
10101110112 = ?16
10 1011 1011
B B
10101110112 = 2BB16

## Slide 40: Octal to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 41: Octal to Hexadecimal
Technique
  Use binary as an intermediary

## Slide 42: Example
10768 = ?16
1 0 7 6
001 000 111 110
10768 = 23E16
2 3 E

## Slide 43: Hexadecimal to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 44: Hexadecimal to Octal
Technique
  Use binary as an intermediary

## Slide 45: Example
1F0C16 = ?8
1 F 0 C
0001 1111 0000 1100
1F0C16 = 174148
1 7 4 1 4

## Slide 46: Exercise – Convert ...
Decimal | Binary | Octal | Hexa- decimal
33 |  |  | 
 | 1110101 |  | 
 |  | 703 | 
 |  |  | 1AF

## Slide 47: Exercise – Convert …
Decimal | Binary | Octal | Hexa- decimal
33 | 100001 | 41 | 21
117 | 1110101 | 165 | 75
451 | 111000011 | 703 | 1C3
431 | 110101111 | 657 | 1AF
Answer